## Slide 1
SMART CONTACTLESS VENDING MACHINE FOR COLLEGES
Capstone Project Phase 2
6 Credits
Project ID : N29
ESA Evaluation
Notes: 1

## Slide 2
TEAM COMPOSITION
Sl.No. | Name | SRN | Photo
1 | PUNATI ROOPESH | PES1UG20EC146 | 
2 | ANKIT RAJ AMBERKAR | PES1UG20EC251 | 
3 | KHAJA TIPPU SULTAN | PES1UG20EC257 | 
4 | RAHUL | PES1UG20EC262 | 
Guide : Prof REKHA S S (ECE)

## Slide 3
Contents
Introduction & Motivation
Summary of Literature
Gaps in literature
Objectives
Problem Statement
Proposed Methodology
Results and Analysis
Conclusion & Future Directions
Project timeline Gantt Chart
References
Project Deliverables

## Slide 4
INTRODUCTION
The “The Smart Contactless Vending Machine for Colleges" is an innovative project that combines web technology, Raspberry Pi computing power, and mechanical components to create a modern and efficient vending machine. The system is designed to offer a seamless user experience through a web-based interface built using Python and the Flask framework.
Web-based Interface: The vending machine's user interface is accessible through a website built using Python and Flask. Users can browse available items, place orders, and complete transactions with ease.
Raspberry Pi 3B Integration: Serving as the brain of the system, the Raspberry Pi 3B handles the processing of orders and controls the physical components. Its GPIO pins are connected to two motors responsible for dispensing the selected items.
QR Code Generation: Upon placing an order on the website, a unique QR code is generated. This QR code encapsulates essential information about the ordered items, including item codes and quantities.
Pi Camera for QR Code Scanning: The Raspberry Pi is equipped with a camera that continuously scans for QR codes. When a user presents their generated QR code to the camera, the system interprets the encoded information.
Motor Triggering Mechanism: Based on the decoded information from the QR code, the Raspberry Pi triggers the corresponding motor to dispense the selected item. This seamless integration ensures an automated and accurate fulfillment process.

## Slide 5
Summary and Gaps in the Literature
Solar Powered Medic Vending Machine:
  Summary:
  - Introduces a solar-powered medical vending machine for areas with limited pharmacy access.- Incorporates various features like user authentication, hygiene maintenance, and temperature check-up.- Aims to address the shortage of first-aid kits in rural areas during emergencies.
  Gaps:
  - Lack of explicit testing procedures and results.
  - Limited information on system scalability.
  - Dependency on a magnetic card for user access could be a barrier in emergency situations.
Research and Application on Vending Machine Data Integration Based on EPC System:
  Summary:
  - Focuses on combining EPC and IoT to improve vending machine efficiency.- Details components like EPC tag data standard, EPCIS, and information exchange in IoT.
  - Emphasizes global identification, middleware efficiency, and PML standardization.
  Gaps:
  - Needs IoT implementations which is not cost effective.
  - Complexity in managing static and dynamic data in a standardized format.

## Slide 6
3. The Cashless Payment Device for Vending Machines - Import Substitution in the Sphere of Vending:
  Summary:
  - Discusses a cashless payment device for vending machines using RFID technology.
  - Highlights user convenience, vending company benefits, and flexible implementation.
  Gaps:
  - Initial setup costs might be high due to specialized devices.
  - Dependency on stable internet connectivity for transactions.- Limitations in functionality in certain environments.
4.New Generation Artificial Intelligent Vending Machine System based on LoRaWan IOT Network:
  Summary:
  - Integrates AI and IoT into vending machines for targeted merchandise sales.
  - Relies on facial recognition for buyer identification and LoRaWAN for data transmission.
  Gaps:
  - Challenges in accurately identifying unique buyer preferences.
  - Potential privacy concerns due to facial recognition.
  - Acknowledgment of the need for careful consideration of drawbacks in implementation.

## Slide 7
5. Smart Vending Machine Based on SMS Gateway For General Transactions:
  Summary:
  - Proposes a smart vending machine using SMS gateway for office stationery transactions.
  - Showcases accessibility, online monitoring, and a backup power system.
  Gaps:
  - Dependency on specific digital payment services.
  - Technical glitches and potential infrastructure limitations.
  - Reliance on stable telecommunication and internet connectivity.
6. A Novel Implementation of FPGA Based Smart Vending Machine :
Summary:
-Presents an FPGA-based vending machine using Verilog HDL platform.
- Simulations, utilization details, and future improvements are discussed.
  Gaps:
  - Limitation in displaying certain messages.
  - Challenges in certain scenarios related to machine response.
  - Reliance on constant adaptation to market changes.

## Slide 8
Objectives
The objective of the project is to create an automated vending machine system with the following key features:
User-Friendly Interface: Provide a web-based interface for users to browse available items, select products, and place orders.
Order Processing: Implement a system for processing user orders within the Flask web application. This involves generating a unique QR code for each order, containing information about the selected items.
QR Code Generation: Dynamically generate QR codes based on the user's order, embedding essential details such as item codes and quantities.
Raspberry Pi Integration: Utilize a Raspberry Pi 3B as the central processing unit to control the vending machine. Integrate the Raspberry Pi with the Flask web application to receive and process user orders.
Camera-Based QR Code Scanning: Set up a Pi camera to scan QR codes. When a user scans their unique QR code using the camera, the Raspberry Pi should interpret the information encoded in the QR code.
Motor Triggering: Based on the decoded information from the QR code, trigger the respective motors connected to the Raspberry Pi GPIO pins to dispense the selected items.
Automation and Efficiency: Create a seamless and efficient vending experience for users, automating the process from order placement on the website to item dispensing through QR code scanning.

## Slide 9
Problem Statement
To design a smart, low powered vending machine with fully digitalised payment options and facilities suitable for university and colleges.

## Slide 10
30/01/23
Capstone Project B.Tech 2018-22 - Feasibility
10
Proposed Methodology
1. Raspberry Pi Web Deployment:
  Utilizing a Raspberry Pi: The choice of Raspberry Pi is driven by its compact size and robust web connectivity capabilities, making it an ideal platform for hosting the vending machine system. The Raspberry Pi acts as the central processing unit, facilitating communication between the web application and the vending machine components.
  Employing Flask: The implementation of Flask, a lightweight web framework for Python, is pivotal in creating a responsive and efficient web application. Flask allows for the development of a user interface that seamlessly interacts with the vending machine system, providing a user-friendly experience.
2. QR Code Generation:
  Unique Product Identifiers: Every product in the vending machine is assigned a unique identifier, ensuring a distinct association with each item.
  Dynamic QR Code Generation: The Flask application dynamically generates QR codes based on the unique product identifiers. These QR codes serve as digital representations of the products, encapsulating essential information such as product details and pricing.
3. Web Interface:
  User-Friendly Interface: The web application hosts a user-friendly interface that enables users to effortlessly browse available products, make selections, and view associated QR codes.
  Seamless User Experience: The goal is to provide a seamless experience, allowing users to initiate transactions and generate QR codes for their chosen products with ease.

## Slide 11
4. QR Code Scanning:
  Device Compatibility: Users can utilize their smartphones or dedicated QR code scanners to read the dynamically generated QR codes presented by the web application.
  Leveraging QR Code Information: The information stored in the QR codes is leveraged to identify the selected product, initiating the subsequent steps in the vending process.
5. Product Dispensing Machine:
  Integration with Vending Machine: The vending machine is intricately linked to the Raspberry Pi and Flask application, establishing a communication bridge. This integration ensures seamless coordination between the web interface and the physical dispensing mechanism.
  Controlled Dispensing System: The system is designed to be secure and controlled, with product dispensing triggered only upon successful QR code scans. This linkage guarantees a synchronized and error-free vending process.
6. Transaction Verification:
  QR Code Validation: The scanned QR codes are verified against a database to ensure their correspondence with valid products within the vending machine inventory.
  Security Measures: Robust security measures are implemented to prevent unauthorized transactions or any potential tampering with the vending system. This includes encryption, authentication protocols, and transaction logs for auditing purposes. The verification process adds an extra layer of assurance, safeguarding the integrity of the vending transactions.

## Slide 12
Raspberry Pi-Based Architecture:
  - Leveraging Raspberry Pi 3 as the core computing unit for its compact size, robust processing capabilities, and web connectivity.
  - Facilitating seamless communication between the web application and vending components, marking a technological advancement.
2. Dynamic QR Codes for Product Interaction:
  - Implementation of dynamic QR codes for efficient product identification and transactions, enhancing user convenience through contactless interactions.
  - Forward-looking approach, emphasizing user-friendly experiences and efficient operations compared to traditional vending machines.
3. Strengths and Highlights of the Project:
  - User-Centric Interface: Prioritizing user-friendly interfaces and QR code scanning with smartphones, improving overall user experience significantly.
  - Hardware and Software Integration: Integration of Raspberry Pi and Flask Framework to ensure an efficient, cohesive system for dispensing products, addressing operational inefficiencies.
4. Adaptability and Multi-Functionality:
  - Focus on digitalized payment options, reduced human intervention for inventory updates, and the introduction of a document printing facility showcase adaptability and sustainability.
  - Sets the project apart from traditional vending machines, offering a multifunctional experience beyond simple product dispensing.
Result and Analysis

## Slide 13
Conclusion:
Enhancement of Vending Experience:
  - Marks a significant leap in enhancing the vending experience within educational institutions.
  - Addresses the need for a smart, low-powered vending machine with fully digitized payment options tailored for universities and colleges.
2. Methodology Highlights:
  - Thoughtful integration of hardware and software components, utilizing Raspberry Pi and Flask.
  - Flask's lightweight nature instrumental in creating a responsive and user-friendly web interface.
  - Dynamic QR code generation and scanning facilitate convenient product selection and transaction initiation.
3. Integration and Security Measures:
  - Raspberry Pi integration ensures controlled dispensing, bolstered by QR code validation for added security.
  - Well-thought-out hardware design incorporating Raspberry Pi 3b+, Pi Cam, and a 5V DC motor.
4. Robust Software Stack:
  - Reliance on Python, Raspbian OS, and Flask demonstrates a robust software stack's efficiency and versatility.
  - Python's readability and flexibility contribute to developing the vending machine's logic.
Conclusion and Future Directions

## Slide 14
Future Directions :
Diversification of Payment Methods
  - Integration of more digital payment options to cater to a wider range of user preferences.
2. Machine Learning for Inventory Management:
  - Use of historical data and usage patterns to optimize inventory levels.
3. Advanced Security Measures:
  - Implementation of biometric authentication or facial recognition to enhance user authentication.
4. Enhanced User Experience and Functionality:
  - Introducing customization features for users and implementing remote monitoring for administrators.
5. Sustainability and Collaboration:
  - Exploration of energy-efficient components and collaboration with campus systems for seamless access and payment integration.
6. Market Expansion and Technological Evolution:
  - Establishment of a foundation for innovative advancements in vending technology.
  - Potential for market expansion beyond educational institutions, showcasing commitment to technological evolution in the vending industry.

## Slide 15
PROJECT TIMELINE
15
 | Week 1 | Week 2 | Week 3 | Week 4 | Week 5 | Week 6 | Week 7 | Week 8 | Week 9 | Week 10 | Week 11 | Week 12 | Week 13 | Week 14 | Week 15
Developing the Hardware parts fixing components |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Creating web page and adding the details of the items and vending machine details |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Creating a Web applications And Connecting it to the hardware |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
testing the Product and fixing all the problems |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 16
Z. Qing and Y. Pu, "Research and application on vending machine data integration based on EPC system," 2011 International Conference on Consumer Electronics, Communications and Networks (CECNet), Xianning, China, 2011, pp. 4304-4306, doi: 10.1109/CECNET.2011.5768255.
V. P. Semenov, V. V. Chernokulsky and N. V. Razmochaeva, "The cashless payment device for vending machines — Import substitution in the sphere of vending," 2017 International Conference "Quality Management,Transport and Information Security, Information Technologies" (IT&QM&IS), St. Petersburg, Russia, 2017, pp. 798-801, doi: 10.1109/ITMQIS.2017.8085948.
S. M. S. Arifin et al., "Smart vending machine based on SMS gateway for general transactions," 2017 15th International Conference on Quality in Research (QiR) : International Symposium on Electrical and Computer Engineering, Nusa Dua, Bali, Indonesia, 2017, pp. 34-39, doi: 10.1109/QIR.2017.8168447.
D. Wibowo and F. Fahmi, "Contactless and Cashless Smart Vending Machine Integrated with Mobile Device," 2021 5th International Conference on Electrical, Telecommunication and Computer Engineering (ELTICOM), Medan, Indonesia, 2021, pp. 146-151, doi: 10.1109/ELTICOM53303.2021.9590103.
M. W. Asyhari, R. Sigit and S. Sukaridhoto, "Vending Machine Monitoring System Integrated with Webserver," 2019 International Electronics Symposium (IES), Surabaya, Indonesia, 2019, pp. 556-559, doi: 10.1109/ELECSYM.2019.8901588.
Y. -B. Park and S. -J. Yoon, "A comparison study of stock-out policies in vending machine systems," 2011 2nd International Conference on Engineering and Industries (ICEI), Seogwipo, Korea (South), 2011, pp. 1-4.
References

## Slide 17
7. M. Suthar, "A Novel Implementation of FPGA Based Smart Vending Machine," 2021 IEEE International Conference on Technology, Research, and Innovation for Betterment of Society (TRIBES), Raipur, India, 2021, pp. 1-6, doi: 10.1109/TRIBES52498.2021.9751636.
8. P. Kumar, S. Singh, M. Choudhary and K. Singh, "Solar Powered Medic Vending Machine," 2020 2nd International Conference on Advances in Computing, Communication Control and Networking (ICACCCN), Greater Noida, India, 2020, pp. 465-468, doi: 10.1109/ICACCCN51052.2020.9362969New
9. D. Wibowo and F. Fahmi, "Contactless and Cashless Smart Vending Machine Integrated with Mobile Device," 2021 5th International Conference on Electrical, Telecommunication and Computer Engineering (ELTICOM), Medan, Indonesia, 2021, pp. 146-151, doi: 10.1109/ELTICOM53303.2021.9590103.
10. C. -C. Hsu, Y. -C. Lin, Y. -L. Shiue and C. -C. Sun, "New Generation Artificial Intelligent Vending Machine System based on LoRaWan IOT Network," 2019 IEEE International Conference on Consumer Electronics - Taiwan (ICCE-TW), Yilan, Taiwan, 2019, pp. 1-2, doi: 10.1109/ICCE-TW46550.2019.8991716

## Slide 18
ADDITIONAL PAPERS REFFERED
1.Design of Energy Efficient LVCMOS based Vending Machine and its Implementation on FPGA
Anupam Yadav5Department of CEA, GLA University,
Mathura, U.P., India
2.30th CIRP Design 2020 (CIRP Design 2020) Design of a Control System for a Vending Machine
3. DESIGN AND IMPLEMENTATION OF VENDING MACHINEUSING VERILOG HDL
P.Pradeepa1, T.Sudhalavanya1, K.Suganthi1,N.Suganthi1, M. Menagadevi 2
4. Design and Implementation of Vending Machine Using Verilog HDL
Akula Vamsi1, Gadiparthi Jagadessh2, Samayamanthula Vikas3, Pika Trisha Srinivas4, Yogesh Kumar Verma5
School of Electronics and Electrical Engineering, Lovely Professional University, Punjab, 144411, India1,

## Slide 19
Deliverables
A fully working vending machine model using Raspberry Pi and sensors
The machine will be able to vend two items.
The machine will be able to print any files that are uploaded in PDF format which can be accessed through a QR-code payment option.
Notification System which can notify the owner about the products. (availability of the items as well as expired products).

## Slide 20
Q & A
Notes: 20